## Slide 1: Nano Processor Design and Implementation
Group 20
Senadheera S.D.A.P. - 240604V
Sangadith K.G.D.N - 240593H
Shanujah S. - 240618R
Saranyu M. - 240295L

## Slide 2: Project Objective
Design and implement a 4-bit NanoProcessor in VHDL capable of executing an 8-instruction ISA, then verify it on the Basys 3 FPGA development board.
Extend functionality with bitwise operations (AND/OR), 4-bit multiplication, and comparison.

## Slide 3: Instruction Set Architecture
Basic design :
Instruction | Description | Instruction
MOVI R, d | Load immediate d into R | 10 RRR 000 dddd
ADD Ra, Rb | Ra = Ra + Rb | 00 RaRaRa RbRbRb 0000
NEG R | R = -R | 01 RRR 0000000
JZR R, d | Jump to d if R == 0 | 11 RRR 0000 ddd

## Slide 4: Instruction Set Architecture
Extended design :
Instruction | Description | Instruction
MOVI R, d | Move immediate value d to register R | 0110 RRRR 000 dddd
ADD Ra, Rb | Ra = Ra + Rb | 0000 RaRaRaRa RbRbRbRb 0000
SUB Ra, Rb | Ra ← Ra − Rb | 0001 RaRaRaRa RbRbRbRb 0000
NEG R | R = -R | 0010 RRRR 0000 0000
AND Ra, Rb | Ra ← Ra & Rb | 0100 RaRaRa RbRbRb 0010
OR Ra, Rb | Ra ← Ra ¦ Rb | 0101 RaRaRa RbRbRb 0000
MUL Ra, Rb | Ra ← Ra × Rb | 0011 RaRaRaRa RbRbRbRb 0101

## Slide 5: Instruction Set Architecture
Extended design :
Instruction | Description | Instruction
CMP Ra, Rb | Compare Ra and Rb, set flags | 1000 RaRaRa RbRbRb 0111 1001 RaRaRa RbRbRb 0111 1010 RaRaRa RbRbRb 0111
JZR R, d | Jump if R == 0 | 0111 RRR 0000 ddd

## Slide 6: Assembly Program and Machine Code
“101110000001", -- MOVI R7,1 ; Initialize R7 to 1 “100100000010", -- MOVI R2,2 ; Initialize R2 to 2 “001110100000", -- ADD R7, R2 ; R7 <= R7 + R2 “100100000011", -- MOVI R2,3 ; Initialize R2 to 3 “001110100000", -- ADD R7,R1 ; Subtract 1 from R2 (Adding negated value) "001110100000", -- ADD R7,R2 ; R7 <= R7 + R2 “110000000101", -- JZR R0,0 ; If R0 == 0, Jump to address 5
Original Version:

## Slide 7: Assembly Program and Machine Code
“01101110000100": MOVI R7,4 ; Initialize R7 to 4
“01101100000010": MOVI R6,2 ; Initialize R6 to 2
“00111111100000": MUL R7,R6 ; R7 ← R7 * R6 = 8
“00001111100000": ADD R7,R6 ; R7 ← R7 + R6 = 10
“10001111100000": EQ R7,R6 ; If R7 == R6, flag set
“10011111100000": GT R7,R6 ; If R7 > R6, flag set
“10101111100000": LT R7,R6 ; If R7 < R6, flag set
“01110000000111": JZR R0, 7 ; If R0 == 0, jump to address
Extended Version:

## Slide 8: System Overview
Core Components:
Program ROM
Program Counter + 3-bit Adder
Instruction Decoder
Register Bank
Adder/Subtractor Unit
7- segment Display LUT
Multi-bit Multiplexers
Additional Components:
Comparator
4-bit Multiplier
Bitwise Operator(AND/OR)

## Slide 9: Data Movement
Bus system was defined to control data movements

## Slide 10: Original Design
Core Control:
Clock: Synchronizes all operations (fetch, decode, execute).
Reset: Initializes registers and program counter to zero.
Data Visibility:
Data: Outputs the value of Register 7 (R7) for real-time monitoring.
S_7Seg & Anodes: Drives the 7-segment display to show R7’s value in hexadecimal.

## Slide 11
Status Flags:
Overflow: Indicates arithmetic overflow
Zero : ALU result is zero
Integration Hub:
Coordinates the Program Counter, Instruction Decoder, ALU, and Register Bank.
Maps internal register states to external displays for validation.
Original Design

## Slide 12
Original Design

## Slide 13
Timing Diagram
Original Design

## Slide 14
Multi-Register Monitoring:
Data_7: Outputs Register 7 (R7) for primary result display
Data_6: Added output for Register 6 (R6), enabling side-by-side operation observation
Advanced Status Flags:
Comparison Flags: Equal, LessThan, GreaterThan for conditional logic
Backward Compatibility: Retains original Zero and Overflow flags
Extended Design

## Slide 15
Extended Design

## Slide 16
Timing Diagram
Original Design

## Slide 17: Core Components

## Slide 18: Program ROM
Key Features:
8-location ROM with 12-bit instructions
Stores hardcoded assembly program
Addressed using 3-bit Program Counter output
Outputs one 12-bit instruction each cycle
Role in Pipeline:
Performs instruction fetch operation
Receives address from the Program Counter
Sends instruction to the Instruction Decoder
Provides instructions sequentially each clock cycle

## Slide 19: Program ROM

## Slide 20: Program Counter & Address Control Logic
3-bit Program Counter (PC):
Function: Store the address of next instruction (0-7).
Update: On slow clock edge, loads PC_Next (from Mux).
Reset: Initializes to 000 on system reset.
3-bit Adder (PC_Adder):
Role: Calculates sequential address (PC_Current + 1).
Example: 010 → 011 (next instruction).

## Slide 21: Program Counter & Address Control Logic
Address_Selector
Inputs:
  Sequential address (PC + 1)
  Jump address (from Instruction Decoder)
Control:
  Jump_Enable signal selects between sequential execution and jump operation.
Output:
  Sends the selected address to the Program Counter (PC_Next).

## Slide 22: Program Counter & Address Control Logic

## Slide 23: Slow Clock
Converts the high-frequency system clock into a slower clock signal (50 MHz → 0.5 Hz).
Allows easier debugging and LED observation.
On each rising edge of the input clock, the counter increments (count = count + 1).
Provides clock signals to the Program Counter and Register Bank.
Synchronizes operations of the Instruction Decoder and ALU.

## Slide 24: Slow Clock

## Slide 25: Instruction Decoder (Original)
Opcode Extraction:
Bits 11–10 are extracted as the opcode to identify the instruction type (MOVI, ADD, NEG, JZR).
Register Control Signals:
Generates Register_Enable, Register_Select_A, and Register_Select_B to select source/destination registers and control register write operations.
ALU Control:
Generates Operation_Select to choose the ALU operation ('0' = ADD, '1' = SUB for NEG instruction).
Immediate Value Handling:
Extracts the lower 4 bits (Instruction(3 downto 0)) as the immediate constant for the MOVI instruction.
Jump Logic (JZR):
Checks whether Register_Value_For_Jump is zero.If zero, Jump_Enable is activated and the jump target address is taken from Instruction(2 downto 0).

## Slide 26: Instruction Decoder (Original)

## Slide 27
Opcode Extraction:
Bits 13–10 are extracted as the 4-bit main opcode to determine the instruction type (ADD, SUB, NEG, MUL, AND, OR, MOVI, JZR, EQ, GT, LT).
ALU Operation Selection:
The extracted 4-bit opcode is passed directly to ALU_Op to control the ALU operation (ADD, SUB, NEG, MUL, AND, OR, comparison operations, etc.).
Register Control Signals:
Generates Register_Enable, Register_Select_A, and Register_Select_B for selecting source and destination registers during ALU execution.
Immediate Value Handling:
Bits 3–0 are extracted as a 4-bit immediate constant for the MOVI instruction when Load_Select = '0’.
Jump Logic (JZR):
Checks whether Register_Value_For_Jump = "0000".If true, Jump_Enable is activated and the jump target address is loaded from bits 2–0.
Instruction Decoder (Extended)

## Slide 28
Instruction Decoder (Extended)

## Slide 29
Instruction Decoder (Extended)

## Slide 30
Instruction Decoder (Extended)

## Slide 31: Load Selector
Purpose:
Selects the data source that will be written into the register bank.
It chooses between the Immediate_Value (used in MOVI instructions) and the computed Register_Value/ALU result.
Control Logic:
Uses a 2-way 4-bit multiplexer (MUX_2W_4B) controlled by the lSlt (Load_Select) signal generated by the instruction decoder.
Selection Operation:
lSlt = '0' → Output receives immediateValue
lSlt = '1' → Output receives registerValue
Output Handling:
The selected 4-bit value is sent to outValue, which is connected to the register write-data path.

## Slide 32: Load Selector

## Slide 33: Register Bank
Key Components:
3-to-8 Decoder: Converts Reg_En into one-hot register enable signals (Reg_Sel). Example: "101" enables R5.
R0 (Zero Register): Permanently stores "0000" and cannot be overwritten.
R1–R7 Registers: General-purpose 4-bit registers. Updated only when their enable signal is active during a clock edge.

## Slide 34: Register Bank
Operation Flow:
Write: Decoder selects a register using Reg_En, and the Data value is stored on the clock edge.
Read: All register outputs are continuously available through Register_Outputs.
Design Features:
Simultaneous access to all register values.
Asynchronous reset clears all registers.
R0 provides a constant zero value for safe ALU operations.

## Slide 35: Register Bank

## Slide 36: Register Data Multiplexer
2-Way 3-Bit Multiplexer:
Selects one of two 3-bit inputs using a single select signal.
Used for choosing between two address or control values in the processor datapath.
2-Way 4-Bit Multiplexer:
Selects one of two 4-bit data inputs based on a control signal.Commonly used for selecting between immediate values and ALU/register outputs.
8-Way 4-Bit Multiplexer:
Selects and outputs one of eight 4-bit inputs using a 3-bit select address.Used for accessing register values from the register bank during CPU operations.
Control Logic:
The select lines determine which input is routed to the output, enabling controlled data transfer within the processor datapath.

## Slide 37: Register Data Multiplexer
2-Way 3-Bit Multiplexer:

## Slide 38: Register Data Multiplexer
2-Way 4-Bit Multiplexer:

## Slide 39: Register Data Multiplexer
8-Way 4-Bit Multiplexer:

## Slide 40: Seven Segment Display
Operation:
Converts a 4-bit binary input (0–15) into the corresponding 7-segment display pattern for hexadecimal output (0–F).
Implementation:
Uses a ROM-based lookup table with 16 entries, where each entry stores a 7-bit segment pattern for the display.
The input address is converted into an integer index to access the correct hexadecimal digit pattern from the ROM.

## Slide 41: Seven Segment Display

## Slide 42: Arithmetic and Logic Unit

## Slide 43: Add_Sub Unit
Addition and Subtraction Calculation: Performs 4-bit addition or subtraction on inputs A_AS and B_AS using the CTRL signal.
CTRL = '0' → Addition (A_AS + B_AS)
CTRL = '1' → Subtraction (A_AS - B_AS) using 2’s complement
Example: 5 (0101) - 3 (0011) → Inverted B_AS = 1100, C_in = 1 → Result = 0010 (2)
Overflow Detection Support:
Product_H stores the upper 4 bits of the 8-bit product.
If Product_H ≠ "0000", the multiplication result exceeds the 4-bit data range, indicating overflow.

## Slide 44: Multiplier Unit

## Slide 45: Multiplier Unit
8-bit Product Calculation:
Multiplies two 4-bit unsigned numbers (A, B) to generate an 8-bit product (full_product).
Example: 4 (0100) × 4 (0100) = 16 (00010000) → Lower 4 bits: 0000 (Product_L) → Upper 4 bits: 0001 (Product_H)
Overflow Detection Support:
Product_H stores the upper 4 bits of the 8-bit product.
If Product_H ≠ "0000", the multiplication result exceeds the 4-bit data range, indicating overflow.

## Slide 46: Multiplier Unit

## Slide 47: Multiplier Unit

## Slide 48: Comparator Unit
Purpose :
Compare two 4-bit signed numbers using 2’s complement representation
Generates three comparison flags :
Equal_Flag
GreaterThan_Flag
LessThan_Flag
How it works :
If Input_A = Input_B , Equal_Flag = ‘ 1 ’
If Input_A < Input_B , LessTHan_Flag = ‘ 1 ’
If Input_A > Input_B , GreaterThan_Flag = ‘ 1 ‘

## Slide 49: Comparator Unit

## Slide 50: Bitwise Operator Unit
Core Functionality: Performs bit-level logic operations between two 4-bit values:
AND: Result = A & B (Bitwise AND)
OR: Result = A | B (Bitwise OR)
XOR: Result = A ^ B (Bitwise XOR)

## Slide 51: Bitwise Operator Unit

## Slide 52: ALU
The Extended_ALU performs multiple 4-bit arithmetic and logic operations based on the 4-bit Op control signal.
0000 → Addition (A + B)
0001 → Subtraction (A - B)
0010 → Negation (0 - B)
0011 → Multiplication (A × B)
0100 → Bitwise AND
0101 → Bitwise OR
1000 → Equal Comparison (A = B)
1001 → Greater Than Comparison (A > B)
1010 → Less Than Comparison (A < B)

## Slide 53: ALU
Key Components:
Arithmetic Logic Unit: Performs arithmetic operations using unsigned binary calculations.
Multiplication Logic: Generates an 8-bit product and returns the lower 4 bits as the result.
Comparison Logic: Produces "0001" when the comparison condition is true, otherwise "0000".
Flag Generation:
  Zero flag becomes '1' when the result equals "0000".
  Overflow flag detects carry-out in arithmetic operations and overflow in multiplication.

## Slide 54: ALU
Zero Detection & Overflow Detection:

## Slide 55: Fundamental Building Blocks
Multiplexers (Data Selectors)
  8-way 4-bit: Uses 3 select lines to route one of eight 4-bit inputs to a single 4-bit output.
  2-way 3-bit: Uses 1 select line to choose between two 3-bit data paths.
  2-way 4-bit: Uses 1 select line to route one of two 4-bit inputs to a single output.
Adders
  Half Adder: Adds 2 bits, outputs Sum and Carry.
  Full Adder: Adds 2 inputs + Carry-in, outputs Sum and Carry-out.
  3-bit Ripple Carry Adder: Cascades 3 Full Adders for 3-bit arithmetic.
  4-bit Ripple Carry Adder: Performs 4-bit addition/subtraction.

## Slide 56: Fundamental Building Blocks
3. Decoders
  2-to-4 Decoder: Takes a 2-bit input and activates exactly one of 4 output lines.
  3-to-8 Decoder: Takes a 3-bit input and drives one of 8 output lines high. Built by cascading two 2-to-4 decoders.
4. 4-bit Register:
  Contains 4 D flip-flops in parallel, each holding one bit. All 4 bits are loaded simultaneously from a 4-bit input bus
  Data is written and read only on the active clock edge

## Slide 57: FPGA Pin Mappings (Original)

## Slide 58: FPGA Pin Mappings (Extended)

## Slide 59: Resource Utilization (Original)

## Slide 60: Resource Utilization (Extended)

## Slide 61: Conclusion
Achievements:
  4-bit Processor: Executes 8+ instructions (arithmetic, logic, control flow).
  Extended Functionality: Added AND/OR/XOR, multiplication, comparisons.
  FPGA Validation: Tested on BASYS3 with real-time 7-segment display output.
Key Learnings:
  Modular Design: Isolated components (ALU, ROM, Decoder) for scalability.
  Signed Arithmetic: Mastered two’s complement & overflow detection.
  Team Collaboration: Streamlined VHDL development & testing.

## Slide 62: Thank You !